## Slide 1: Hardware Design Issues
Custom Single-Purpose Processor - Hardware

## Slide 2: Combinational and Sequential logic
Combinational circuit is a type of logic circuit whose output is a function of only the present input.
Sequential logic is a type of logic circuit whose output depends not only on the present value of its input signals but on the sequence of past inputs, the input history as well.

## Slide 3: Combinational and Sequential logic
Transistor:
  The basic electrical component in digital systems.
  Acts as an on/off switch.
  Voltage at “gate” controls whether current flows from source to drain.
  Don’t confuse this “gate” with a logic gate.
gate
source
drain
Conducts
if gate=1
source
drain
oxide
gate
IC package
IC
channel
Silicon substrate

## Slide 4: CMOS transistor implementations
Complementary Metal Oxide Semiconductor:
We refer to logic levels
  Typically 0 is 0V, 1 is 5V
Two basic CMOS types
  nMOS conducts if gate=1
  pMOS conducts if gate=0
  Hence “complementary”
Basic gates
  Inverter, NAND, NOR
gate
source
drain
nMOS
Conducts
if gate=1
gate
source
drain
pMOS
Conducts
if gate=0
x
F = x'
1
inverter
0
F = (xy)'
x
1
x
y
y
NAND gate
0
1
F = (x+y)'
x
y
x
y
NOR gate
0

## Slide 5: Basic logic gates
F = x y
AND
F = (x y)’
NAND
F = x  y
XOR
F = x
Driver
F = x’
Inverter
x
F
F = x + y
OR
F = (x+y)’
NOR
x
F
x
y
F
F
x
y
x
y
F
x
y
F
x
y
F
F = x y
XNOR
F
y
x
x
0
y
0
F
0
0
1
0
1
0
0
1
1
1
x
0
y
0
F
0
0
1
1
1
0
1
1
1
1
x
0
y
0
F
0
0
1
1
1
0
1
1
1
0
x
0
y
0
F
1
0
1
0
1
0
0
1
1
1
x
0
y
0
F
1
0
1
1
1
0
1
1
1
0
x
0
y
0
F
1
0
1
0
1
0
0
1
1
0
x
F
0
0
1
1
x
F
0
1
1
0

## Slide 6: Combinational logic design
A) Problem description
y is 1 if a is to 1, or b and c are 1.
z is 1 if b or c is to 1, but not both, or if all are 1.
D) Minimized output equations
00
0
1
01
11
10
0
1
0
1
0
1
1
1
a
bc
y
y = a + bc
00
0
1
01
11
10
0
0
1
0
1
1
1
1
z
z = ab + b’c + bc’
a
bc
C) Output equations
y = a'bc + ab'c' + ab'c + abc' + abc
z = a'b'c + a'bc' + ab'c + abc' + abc
B) Truth table
1
0
1
1
1
1
1
0
1
1
1
1
1
1
1
0
0
1
0
1
0
1
0
0
1
0
1
1
1
0
1
0
0
1
0
0
0
0
0
0
Inputs
a
b
c
Outputs
y
z
E) Logic Gates
a
b
c
y
z

## Slide 7: Combinational components
With enable input e  all O’s are 0 if e=0
With carry-in input Ci
sum = A + B + Ci
May have status outputs carry, zero, etc.
O =
I0 if S=0..00
I1 if S=0..01
…
I(m-1) if S=1..11
O0 =1 if I=0..00
O1 =1 if I=0..01
…
O(n-1) =1 if I=1..11
sum = A+B
(first n bits)
carry = (n+1)’th
bit of A+B
less = 1 if A<B
equal =1 if A=B
greater=1 if A>B
O = A op B
op determined
by S.
n-bit, m x 1
Multiplexor
O
…
S0
S(log m)
n
n
I(m-1)
I1
I0
…
log n x n
Decoder
…
O1
O0
O(n-1)
I0
I(log n -1)
…
n-bit
Adder
n
A
B
n
sum
carry
n-bit
Comparator
n
n
A
B
less
equal
greater
n bit,
m function
ALU
n
n
A
B
…
S0
S(log m)
n
O

## Slide 8: Sequential components
Q =
0 if clear=1,
I if load=1 and clock=1,
Q(previous) otherwise.
Q =
0 if clear=1,
Q(prev)+1 if count=1 and clock=1.
clear
n-bit
Register
n
n
load
I
Q
shift
I
Q
n-bit
Shift register
n-bit
Counter
n
Q
Q = lsb
- Content shifted
- I stored in msb

## Slide 9: Sequential logic design
A) Problem Description
You want to construct a clock divider. Slow down your pre-existing clock so that you output a 1 for every four clock cycles
0
1
2
3
x=0
x=1
x=0
x=0
a=1
a=1
a=1
a=1
a=0
a=0
a=0
a=0
B) State Diagram
C) Implementation Model
Combinational logic
State register
a
x
I0
I0
I1
I1
Q1
Q0
D) State Table (Moore-type)
1
0
1
1
1
1
1
0
1
1
1
1
1
0
0
0
0
1
0
1
0
1
0
0
1
0
1
1
1
0
1
0
0
1
0
0
0
0
0
0
Inputs
Q1
Q0
a
Outputs
I1
I0
1
0
0
0
x
Given this implementation model
  Sequential logic design quickly reduces to combinational logic design

## Slide 10: Sequential logic design (cont.)
0
0
1
Q1Q0
I1
I1 = Q1’Q0a + Q1a’ + Q1Q0’
0
1
1
1
0
1
0
00
11
10
a
01
0
0
0
1
0
1
1
00
01
11
a
1
10
I0
Q1Q0
I0 = Q0a’ + Q0’a
0
1
0
0
0
1
1
0
0
00
01
11
10
x = Q1Q0
x
0
1
0
a
Q1Q0
E) Minimized Output Equations
F) Combinational Logic
a
Q1
Q0
I0
I1
x

## Slide 11: Custom single-purpose processor basic model
controller and datapath
controller
datapath
…
…
external
control
inputs
external
control outputs
…
external
data
inputs
…
external
data
outputs
datapath
control
inputs
datapath
control
outputs
…
…
a view inside the controller and datapath
controller
datapath
…
…
state
register
next-state
and
control
logic
registers
functional
units

## Slide 12: Example: greatest common divisor
GCD
(a) black-box view
x_i
y_i
d_o
go_i
0: int x, y;
1: while (1) {
2: while (!go_i);
3: x = x_i;
4: y = y_i;
5: while (x != y) {
6: if (x < y)
7: y = y - x;
else
8: x = x - y;
}
9: d_o = x;
}
(b) desired functionality
y = y -x
7:
x = x - y
8:
6-J:
x!=y
5:
!(x!=y)
x<y
!(x<y)
6:
5-J:
1:
1
!1
x = x_i
3:
y = y_i
4:
2:
2-J:
!go_i
!(!go_i)
d_o = x
1-J:
9:
(c) state diagram
First create algorithm
Convert algorithm to “complex” state machine
  Known as FSMD: finite-state machine with datapath
  Can use templates to perform such conversion

## Slide 13: State diagram templates
Assignment statement
a = b
next statement
a = b
next statement
Loop statement
while (cond) {
loop-body-
statements
}
next statement
loop-body-
statements
cond
next statement
!cond
J:
C:
Branch statement
if (c1)
c1 stmts
else if c2
c2 stmts
else
other statements
next statement
c1
c2 stmts
!c1*c2
!c1*!c2
next statement
others
c1 stmts
J:
C:

## Slide 14: Creating the datapath
Create a register for any declared variable
Create a functional unit for each arithmetic operation
Connect the ports, registers and functional units
  Based on reads and writes
  Use multiplexors for multiple sources
Create unique identifier
  for each datapath component control input and output
y = y -x
7:
x = x - y
8:
6-J:
x!=y
5:
!(x!=y)
x<y
!(x<y)
6:
5-J:
1:
1
!1
x = x_i
3:
y = y_i
4:
2:
2-J:
!go_i
!(!go_i)
d_o = x
1-J:
9:
subtractor
subtractor
7: y-x
8: x-y
5: x!=y
6: x<y
x_i
y_i
d_o
0: x
0: y
9: d
n-bit 2x1
n-bit 2x1
x_sel
y_sel
x_ld
y_ld
x_neq_y
x_lt_y
d_ld
<
5: x!=y
!=
Datapath

## Slide 15: Creating the controller’s FSM
Same structure as FSMD
Replace complex actions/conditions with datapath configurations
y = y -x
7:
x = x - y
8:
6-J:
x!=y
5:
!(x!=y)
x<y
!(x<y)
6:
5-J:
1:
1
!1
x = x_i
3:
y = y_i
4:
2:
2-J:
!go_i
!(!go_i)
d_o = x
1-J:
9:
y_sel = 1
y_ld = 1
7:
x_sel = 1
x_ld = 1
8:
6-J:
x_neq_y
5:
!x_neq_y
x_lt_y
!x_lt_y
6:
5-J:
d_ld = 1
1-J:
9:
x_sel = 0
x_ld = 1
3:
y_sel = 0
y_ld = 1
4:
1:
1
!1
2:
2-J:
!go_i
!(!go_i)
go_i
0000
0001
0010
0011
0100
0101
0110
0111
1000
1001
1010
1011
1100
Controller
subtractor
subtractor
7: y-x
8: x-y
5: x!=y
6: x<y
x_i
y_i
d_o
0: x
0: y
9: d
n-bit 2x1
n-bit 2x1
x_sel
y_sel
x_ld
y_ld
x_neq_y
x_lt_y
d_ld
<
5: x!=y
!=
Datapath

## Slide 16: Splitting into a controller and datapath
y_sel = 1
y_ld = 1
7:
x_sel = 1
x_ld = 1
8:
6-J:
x_neq_y=1
5:
x_neq_y=0
x_lt_y=1
x_lt_y=0
6:
5-J:
d_ld = 1
1-J:
9:
x_sel = 0
x_ld = 1
3:
y_sel = 0
y_ld = 1
4:
1:
1
!1
2:
2-J:
!go_i
!(!go_i)
go_i
0000
0001
0010
0011
0100
0101
0110
0111
1000
1001
1010
1011
1100
Controller
Controller implementation model
y_sel
x_sel
Combinational logic
Q3
Q0
State register
go_i
x_neq_y
x_lt_y
x_ld
y_ld
d_ld
Q2
Q1
I3
I0
I2
I1
subtractor
subtractor
7: y-x
8: x-y
5: x!=y
6: x<y
x_i
y_i
d_o
0: x
0: y
9: d
n-bit 2x1
n-bit 2x1
x_sel
y_sel
x_ld
y_ld
x_neq_y
x_lt_y
d_ld
<
5: x!=y
!=
(b) Datapath

## Slide 17: Controller state table for the GCD example
Inputs
Outputs
Q3
Q2
Q1
Q0
x_neq_y
x_lt_y
go_i
I3
I2
I1
I0
x_sel
y_sel
x_ld
y_ld
d_ld
0
0
0
0
*
*
*
0
0
0
1
X
X
0
0
0
0
0
0
1
*
*
0
0
0
1
0
X
X
0
0
0
0
0
0
1
*
*
1
0
0
1
1
X
X
0
0
0
0
0
1
0
*
*
*
0
0
0
1
X
X
0
0
0
0
0
1
1
*
*
*
0
1
0
0
0
X
1
0
0
0
1
0
0
*
*
*
0
1
0
1
X
0
0
1
0
0
1
0
1
0
*
*
1
0
1
1
X
X
0
0
0
0
1
0
1
1
*
*
0
1
1
0
X
X
0
0
0
0
1
1
0
*
0
*
1
0
0
0
X
X
0
0
0
0
1
1
0
*
1
*
0
1
1
1
X
X
0
0
0
0
1
1
1
*
*
*
1
0
0
1
X
1
0
1
0
1
0
0
0
*
*
*
1
0
0
1
1
X
1
0
0
1
0
0
1
*
*
*
1
0
1
0
X
X
0
0
0
1
0
1
0
*
*
*
0
1
0
1
X
X
0
0
0
1
0
1
1
*
*
*
1
1
0
0
X
X
0
0
1
1
1
0
0
*
*
*
0
0
0
0
X
X
0
0
0
1
1
0
1
*
*
*
0
0
0
0
X
X
0
0
0
1
1
1
0
*
*
*
0
0
0
0
X
X
0
0
0
1
1
1
1
*
*
*
0
0
0
0
X
X
0
0
0

## Slide 18: Completing the GCD custom single-purpose processor design
We finished the datapath
We have a state table for the next state and control logic
  All that’s left is combinational logic design
This is not an optimized design, but we see the basic steps
…
…
a view inside the controller and datapath
controller
datapath
…
…
state
register
next-state
and
control
logic
registers
functional
units

## Slide 19: RT-level custom single-purpose processor design
We often start with a state machine
  Rather than algorithm
  Cycle timing often too central to functionality
Example
  Bus bridge that converts 4-bit bus to 8-bit bus
  Start with FSMD
  Known as register-transfer (RT) level
  Exercise: complete the design
Problem Specification
Bridge
A single-purpose processor that converts two 4-bit inputs, arriving one at a time over data_in along with a rdy_in pulse, into one 8-bit output on data_out along with a rdy_out pulse.
Sender
data_in(4)
rdy_in
rdy_out
data_out(8)
Receiver
clock
FSMD
WaitFirst4
RecFirst4Start
data_lo=data_in
WaitSecond4
rdy_in=1
rdy_in=0
RecFirst4End
rdy_in=1
RecSecond4Start
data_hi=data_in
RecSecond4End
rdy_in=1
rdy_in=0
rdy_in=1
rdy_in=0
Send8Start
data_out=data_hi & data_lo
rdy_out=1
Send8End
rdy_out=0
Bridge
rdy_in=0
Inputs
rdy_in: bit; data_in: bit[4];
Outputs
rdy_out: bit; data_out:bit[8]
Variables
data_lo, data_hi: bit[4];

## Slide 20
RT-level custom single-purpose processor design (cont’)
WaitFirst4
RecFirst4Start
data_lo_ld=1
WaitSecond4
rdy_in=1
rdy_in=0
RecFirst4End
rdy_in=1
RecSecond4Start
data_hi_ld=1
RecSecond4End
rdy_in=1
rdy_in=0
rdy_in=1
rdy_in=0
Send8Start
data_out_ld=1
rdy_out=1
Send8End
rdy_out=0
(a) Controller
rdy_in
rdy_out
data_lo
data_hi
data_in(4)
(b) Datapath
data_out
data_out_ld
data_hi_ld
data_lo_ld
clk
to all registers
data_out
Bridge

## Slide 21: Optimizing single-purpose processors
Optimization is the task of making design metric values the best possible
Optimization opportunities
  original program
  FSMD
  datapath
  FSM

## Slide 22: Optimizing the original program
Analyze program attributes and look for areas of possible improvement
  number of computations
  size of variable
  time and space complexity
  operations used
    multiplication and division very expensive

## Slide 23: Optimizing the original program (contd)
0: int x, y;
1: while (1) {
2: while (!go_i);
3: x = x_i;
4: y = y_i;
5: while (x != y) {
6: if (x < y)
7: y = y - x;
else
8: x = x - y;
}
9: d_o = x;
}
0: int x, y, r;
1: while (1) {
2: while (!go_i);
// x must be the larger number
3: if (x_i >= y_i) {
4: x=x_i;
5: y=y_i;
}
6: else {
7: x=y_i;
8: y=x_i;
}
9: while (y != 0) {
10: r = x % y;
11: x = y;
12: y = r;
}
13: d_o = x;
}
original program
optimized program
replace the subtraction operation(s) with modulo operation in order to speed up program
GCD(42, 8) - 9 iterations to complete the loop
x and y values evaluated as follows : (42, 8), (34, 8), (26,8), (18,8), (10, 8), (2,8), (2,6), (2,4), (2,2).
GCD(42,8) - 3 iterations to complete the loop
x and y values evaluated as follows: (42, 8), (8,2), (2,0)

## Slide 24: Optimizing the FSMD
Areas of possible improvements
  merge states
    states with constants on transitions can be eliminated, transition taken is already known
    states with independent operations can be merged
  separate states
    states which require complex operations (a*b*c*d) can be broken into smaller states to reduce hardware size
  scheduling

## Slide 25: Optimizing the FSMD (cont.)
int x, y;
2:
go_i
!go_i
x = x_i
y = y_i
x<y
x>y
y = y -x
x = x - y
3:
5:
7:
8:
d_o = x
9:
y = y -x
7:
x = x - y
8:
6-J:
x!=y
5:
!(x!=y)
x<y
!(x<y)
6:
5-J:
1:
1
!1
x = x_i
y = y_i
4:
2:
2-J:
!go_i
!(!go_i)
d_o = x
1-J:
9:
int x, y;
3:
original FSMD
optimized FSMD
eliminate state 1 – transitions have constant values
merge state 2 and state 2J – no loop operation in between them
merge state 3 and state 4 – assignment operations are independent of one another
merge state 5 and state 6 – transitions from state 6 can be done in state 5
eliminate state 5J and 6J – transitions from each state can be done from state 7 and state 8, respectively
eliminate state 1-J – transition from state 1-J can be done directly from state 9

## Slide 26: Optimizing the datapath
Sharing of functional units
  one-to-one mapping, as done previously, is not necessary
  if same operation occurs in different states, they can share a single functional unit
Multi-functional units
  ALUs support a variety of operations, it can be shared among operations occurring in different states

## Slide 27: Optimizing the FSM
State minimization
  task of merging equivalent states into a single state
    state equivalent if for all possible input combinations the two states generate the same outputs and transitions to the next same state